## Slide 1: Robot rover shield
For Arduino or Keyestudio MEGA 2560 , Due , Hitex ShiledBuddy TC275 or TC375, Adafruit ntral M4 Express

## Slide 2: Ports
A
B
C
D

## Slide 3: A – Section (navigation sensors)
PS2 controller:
3V3 GND CLK(29) ATT(27) COM(25) DATA(23)
blue green gray white
Ultrasonic (LEFT):
5V GND ECHO(33) TRIGGER(31)
Ultrasonic (RIGHT):
5V GND ECHO(37) TRIGGER(35)
Ultrasonic (CENTER):
5V GND ECHO(41) TRIGGER(39)
D1:
5V GND SIG(43)
D2:
5V GND SIG(45)
D3:
5V GND SIG(47)
HC-SR04 Ultrasonic sensors:
4k7Ω & 2k7Ω Voltage divider required on ECHO pin ???

## Slide 4: ADUINO & Ultrasonic sensor

## Slide 5: B – Section (SD card & analog Input)
SPI SD card:
GND 5V MISO(50) MOSI(51) SCK(52) CS(53)
A7:
SIG(A15) GND 5V
A6:
SIG(A14) GND 5V
VBat:
SIG(A11)
Button:
SIG(A10)
Buttons for:
SIG(A10)

## Slide 6: C – Section (Sensors & Motor control)
Temperature sens.:
SIG(46) GND 5V
Rain drop sensor:
SIG(A6) GND 5V SIG(40)
Current sens.:
SIG(A5) GND 5V
A5 – A1:
SIG(A4 – A0) GND 5V
MB_Controll:
GND DIR_B1(28) DIR_B2(26) PWM_B(3)
MA_Controll:
GND DIR_A1(22) DIR_A2(24) PWM_A(2)
MA_Encoder:
SIG(4) GND 5V
MB_Encoder:
SIG(5) GND 5V
P1-P7:
SIG(7-13) GND 5V

## Slide 7: D – Section (I2C & Serial communication)
DS3231 RTC (0x57 I2C):
5V GND SDA SCL
I2C (free I2C):
5V GND SDA SCL
BNO055 9-DOF Compass
(0x28 I2C): 5V GND SDA SCL
LCD2004 (0x27, I2C):
5V GND SDA SCL
GSM (1):
TX1 RX1 GND
GPS (2):
TX2 RX2 GND
XBEE (3):
TX3 RX3 GND
Maual/Auto:
5V GND SIG(6)
TX0 /RX0 is for Jetson Nano on normal serial connector !
(Current mearument: ADS1115
ADDR pin to GND -> 0x48)
Flip in RTC the GND & 5V positions !!!:

## Slide 8: Power management (for 5V MCUs)
12V IN
for 2 motors, shield & MCU
For main & safety switch
12V OUT
or 2 motors
12V or 24V to 5V mini buck converter. This can be replaced to 12V to 3V3 for DUE
5V to 3V3 regulator for PS2 only
Jumper for PS2 5V? or 3V3
Jumper for 5V IN
5V from buck power supply
Jumper for 12V IN
(not in use)
Fuses

## Slide 9: Power measurement
Current measurrment
ACS712 (30A)
5V Sig GND
Sig to ADS1115’s A3
ADS1115
ACS712 Sig to ADS1115’s A3
10k/10k to ADS1115’s A2
SCL SDA GND 5V
2x 10kΩ voltage divider for ADS1115
10kΩ & 47kΩ (measre before soldering !) BatRs[] = voltage deivider for battery volt measurement Signal to A11
1kΩ & LM4040_2.5 V
for V ref
Or connect signal
of ACS712 to A5
ADS1115
ADDR pin to GND -> 0x48
Mesure internal ref 2.56V with separayte Arduin sketch as well ! Measure_intRefVolt.ino

## Slide 10: How use jumpers for 3V3 MCU’s (Due etc.)
Populate here 3V3 regulator only
No regulator req. here. Use 3V3 PS2 only !
Jumper for 3V3 IN
3V3 from buck power supply
Jumper for PS2 put on 3V3

## Slide 11
https://www.youtube.com/watch?v=E8GqHvOK4DI&t=646s

## Slide 12: Vref: setup external reference voltage for accurate measurment
5V from “5V” pin of the MCU
Bypass jumper to make a separate small PCB for Vref (ferrite signal susp etc.)
GND & 5V for Vref PCB
Signal out on Ref pin

## Slide 13: V ref mini PCB for improvement