## Slide 1
I'm mechanical engineer from Hungary, but working in India in quality leader position.
As a passion, I started to work on a robot rover shield for Arduino MEGA.
One of the main goals is to come up with a generic, but versatile shield, which can be interesting for others as well.
The following features are already included:
- 2 DC motor control 2x (pwm + dir1/dir2) for external motor driver.
- 2 encoder input (magnetic type)
- battery volt & capacity measurement ;)
- rain sensor
- I2C: 4x20 LCD display
- I2C: 9 DOF IMU (Bosch BNO055)
- 3 ultrasonic distance sensor(left, right & ceter)
- 3+ momentary buttons
- PS2 controller for manual mode
- XBee, GSM, GPS on serial port 1-3
- Jetson Nano on serial 0 (for visual servoing with simple webcam)
More can be added:
- head light control
- 3? servo motor control
- ...
I made the draft schematics & PCB in KiCad.
Draft scripts in C++ and in Python for Jetson Nano are available
and a 1m x 1m x 0.5m rover as well to test, how all works together. ;)
As of now, I'm the only one in the project and about to finalize the schematic & PCB.
If Your are in, kindly let me know.
Thank You for your help and support in advance.
Warm Regards,
Andras
andras.steger@protonmail.com

## Slide 2
Keyestudio MEGA 2560 Compatible Board Advanced
Motor controller LEFT side
Motor controller RIGHT side
Battery voltage
Battery current
Battery temperature
GPS
GSM
Jetson Nano
XBee
PS2 controller (3V3)
Analog pins
Digital pins
Digital/pwm pins
Serial pins
Digital pins
Rain drop sensor
Ambient temp.
3 ultrasonic distance sensors
5 buttons
I2C
4x20 LCD panel
IMU
AMS1117 – 1A
NSP1117 – 1A
MP2307DN - 2A or 3A ?
MP2308DN - 4A
https://wiki.keyestudio.com/Ks0342_Keyestudio_MEGA_2560_Compatible_Board_Advanced

## Slide 4
Adafruit Grand Central M4 Express featuring the SAMD51
https://www.adafruit.com/product/4064

## Slide 5
WEEDINATOR/docs/TC275.pdf
@ SembazuruCDE: Thank You for the suggestion, I was not aware with this board.
Actually this is the second part, which is to be revised: overall control MCU.
If I put more time-consuming stuff then the speed go slow.
Checking the sensors and control the motor + GPS + XBee.
I attached the planned components. (red is where the 3V3 is not possible.)
I was thinking on these MCUs:
Ks0342 Keyestudio MEGA 2560
https://wiki.keyestudio.com/Ks0342_Keyestudio_MEGA_2560_Compatible_Board_Advanced
(5V 2A regulator onboard and improved 3.3V regulator, that can run from a +12V supply.)
Hitex ShieldBuddyTC275 – AURIX™
https://www.infineon.com/cms/en/product/evaluation-boards/kit_aurix_tc275_ard_sb/
(Infineon TC275 32-bit 3 core processor, but very expensive)
Or just use 2 MEGA with same Shield (different components are soldered according to the role.)

## Slide 6
https://www.ehitex.de/en/starter-kits/for-aurix/2693/hitex-shieldbuddytc375-aurix-powered-arduino-uno-r3-hardware-compatible-platform

## Slide 7
https://free-entry-toolchain.hightec-rt.com/

## Slide 8
 | MEGA | Due | Keyestudio MEGA 2560 Advanced | Grand Central M4 Express | Hitex ShieldBuddy TC275 | ESP32 | Teensy 4.1
CPU | ATMEGA2560-16AU | Atmel SAM3X8E ARM Cortex-M3 | ATMEGA2560-16AU | Cortex M4 SAMD51 | AURIX TC275 | Xtensa | Cortex-M7
CPU speed | 16 MHz | 84 MHz | 16 MHz | 120 MHz | 200 MHz (each core sep.) | 160 or 240 MHz | 600 MHz
Bit | 8 | 32 | 8 | 32 | 32 | 32 | 32
Core | 1 | 1 | 1 | 1 | 3 | 1/2 | 1
Prog. Flash | 256 kB | 512 kB | 256 kB | 1 MB | 4 MB | 520 kB | 8 MB
RAM/Data Flash | 8 kB | 96 kB | 8 kB | 256 kB | 384 kB |  | 1 MB
QSPI Flash |  |  |  | 8 MB |  |  | 
Logic level | 5 V | 3.3V | 5V | 3.3V | 5V |  | 3.3V
DC Current per I/O Pin | 20 mA | 130 mA (all I/O lines) | 20 mA |  |  |  | 4mA
DC Curr. for 3.3V Pin | 50 mA | 50 mA | 50 mA |  |  |  | 
DC Curr. out on 5V Pin | 0.8 A | 0.8 A | 2A |  |  |  | 
Dig. pins | 54 | 54 (12 PWM) | 54 (15 PWM) | 70 (22 PWM) | 64 | 16 PWM+motor | 40 (35 PWM)
Analog pins | 16 | 12 (ADC 12 bit) | 16 | 15 | 48+12 |  | 18
UART |  4 | 4 | 4 |  |  | 3 | 8
I2C |  |  |  |  |  | 2 + (I2S) 2 | 3
CAN |  |  |  |  |  4 nodes |  | 3
SPI |  |  |  |  |  | 4 | 3
Ext. interrupt | 2, 3, 18, 19, 20, 21 | All digital pins |  |  |  |  | 
Extra |  |  |  | Micro SD card CircuitPython |  | WiFi, BT | Micro SD card Ethernet, mem exp.

## Slide 9
 | MEGA | Due | Keyestudio MEGA 2560 Advanced | Grand Central M4 Express | Hitex ShieldBuddy TC275 | Hitex ShieldBuddy TC375 | KIT_A2G_TC375_LITE
CPU | ATMEGA2560-16AU | Atmel SAM3X8E ARM Cortex-M3 | ATMEGA2560-16AU | Cortex M4 SAMD51 | AURIX TC275 | AURIX TC375 | 
CPU speed | 16 MHz | 84 MHz | 16 MHz | 120 MHz | 200 MHz (each core sep.) | 300 MHz | 
Bit | 8 | 32 | 8 | 32 | 32 | 32 | 
Core | 1 | 1 | 1 | 1 | 3 | 3 | 
Prog. Flash | 256 kB | 512 kB | 256 kB | 1 MB | 4 MB | Up 6 MB flash | 
RAM/Data Flash | 8 kB | 96 kB | 8 kB | 256 kB | 384 kB | Up to 1.1 MB SRAM | 
QSPI Flash |  |  |  | 8 MB |  |  | 
Logic level | 5 V | 3.3V | 5V | 3.3V | 5V |  | 
DC Current per I/O Pin | 20 mA | 130 mA (all I/O lines) | 20 mA |  |  |  | 
DC Curr. for 3.3V Pin | 50 mA | 50 mA | 50 mA |  |  |  | 
DC Curr. out on 5V Pin | 0.8 A | 0.8 A | 2A |  |  |  | 
Dig. pins | 54 | 54 (12 PWM) | 54 (15 PWM) | 70 (22 PWM) | 64 | 128x DMA channels | 
Analog pins | 16 | 12 (ADC 12 bit) | 16 | 15 | 48+12 | Up to 104x ADC channels | 
UART |  4 | 4 | 4 |  |  |  | 
I2C |  |  |  |  |  |  | 
CAN |  |  |  |  |  4 nodes | 8xCAN FD | 
SPI |  |  |  |  |  |  | 
Ext. interrupt | 2, 3, 18, 19, 20, 21 | All digital pins |  |  |  |  | 
Extra |  |  |  | Micro SD card CircuitPython |  |  | 

## Slide 10
https://www.infineon.com/cms/en/product/microcontroller/32-bit-tricore-microcontroller/32-bit-tricore-aurix-tc3xx/aurix-family-tc37xtp/

## Slide 11
– Application Kit TC397 V2.0 with VEXT=5V
– Application Kit TC397 V2.0 with VEXT=3,3V
– Application Kit TC387 V2.0 with VEXT=5V
– Application Kit TC387 V2.0 with VEXT=3,3V
https://copperhilltech.com/blog/arduino-due-can-bus-controller-area-network-interfaces/
https://aurduino.boards.net/
Welcome to the ShieldBuddy forum!

## Slide 12
MCU 1
(can be slow)
MCU 2
(must be fast)
GNSS/GPS
Compass
Serial com.
Heading
Bearing
Coordinates
Distance from waypoint
Motor drive
Motor remote control (PS2)
LCD display
Jetson Nano
(must be fast)
Serial com.
Advanced object recognition
Bat. Volt & current measure.
Rain & amb. temperature sensor
Ultrasonic distance sensor
Camera
Information flow
GSM/GPRS/SMS
GSM/GPRS/SMS
Push buttons for status
Audio ?

## Slide 13
Jetson Nano 4GB B01
Robot Rover Shield on MEGA
RX0/TX0
HC-SR04
5V/15mA
(Volt divider 4.7kΩ & 2.7kΩ
required on Echo pin)
Trig/EchoL D31/33
Trig/EchoR D35/37
Trig/EchoC D39/41
RX3/TX3
XBee 2mW or 63mW 3V3
SIM808 GSM/GPRS/GPS Module with GPS and GSM Antenna
RX1/TX1
SCL
SDA
BNO055 9-DOF (0x28)
3V3 or 5V
LCD2004 LCD with I2C
(0x27) 5V/40mA
(negative voltage generator
to be soldered on the back)
A2 or D49,D51,D53
Momentary push buttons (x3) with proper resistors
A0
Divided voltage from Vcc=12V for battery terminal volt measurement
DS18B20 Temperature Sensor 3.0 – 5.5V
A1
ACS712 30A; 3.3-5V
or INA 213
D5
Rain drop sensor
A&D output; 3V3 - 5V
D52/A14
PWM Left / Right
Enable Left1/Left2
Encoder Left / Right
Enable Right1/Right2
D2/D3
D32/D36
D4/D5
D40/D44
PS2 wireless remote 2.4GHz; 3V3
D23,D25,D27,D29
Simple webcam
https://forum.arduino.cc/index.php?topic=723271.0
5V as well as
3.3V logic levels

## Slide 14
SPI SD card
https://www.youtube.com/watch?v=5Dp-XatLySM
https://howtomechatronics.com/tutorials/arduino/arduino-sd-card-data-logging-excel-tutorial/
50, 51, 52, 53
DS3231 Real Time Clock
With temp. sens
0x57
https://howtomechatronics.com/tutorials/arduino/arduino-ds3231-real-time-clock-tutorial/

## Slide 15
https://www.element14.com/community/groups/roadtest/blog/2019/06/15/converting-5v-lcds-to-33v
https://www.element14.com/community/view-product.jspa?fsku=9663703&nsku=61J6203&COM=noscript
ICL7660CBAZ
MC1206F106Z100CT
https://in.element14.com/multicomp/mc1206f106z100ct/cap-10-f-10v-y5v-1206/dp/1759434?COM=referral-cmty-noscript
10 µF, 10 V, 1206 [3216 Metric], +80%, -20%, Y5V, MC Serie
MCWR04X2201FTL
two 10µF capacitors across pads marked C3 and C4
ICL7660
2.2k Ohm resistor across pad R6
https://in.element14.com/multicomp/mcwr04x2201ftl/res-2k2-1-0-0625w-thick-film/dp/2447148?st=2k2
How to convert 5V 4x20 LCD to 3V3:

## Slide 17
12V
LiFePO4
Buck regulator or LM7833
+3.3V

## Slide 18
1N4001
R2
R3
12V
LiFePO4
78033V3
To buck converter
ACS712
R1
For external reference
15 A
1 A
To 2 x motor controller power
15 A
From buck converter
For battery volt meter
3xI2C
* PS2 controller ** 3xUltras. Distance *** Motor Direction **** 3xPush buttons
***** PWM, encoder etc.
*
**
***
*****
JST-XH 2.5mm
With 2,3,4,7 pins
4xSerial
****
!
!
100n
(ceramic)

## Slide 19
1N4001
R2
R3
12V
LiFePO4
78033V3
To buck converter
ACS712
R1
For external reference
15 A
1 A
To 2 x motor controller power
15 A
From buck converter
For battery volt meter
3xI2C
* PS2 controller ** 3xUltras. Distance *** Motor Direction **** 3xPush buttons
***** PWM, encoder etc.
*
**
***
*****
JST-XH 2.5mm
With 2,3,4,7 pins
4xSerial
****
!
100n
(ceramic)
B
A

## Slide 20
1N4001
R2
R3
12V
LiFePO4
To buck converter
ACS712
R1
For external reference
78333V3
15 A
1 A
To 2 x motor controller power
15 A
From buck converter
For battery volt meter
3xI2C
* PS2 controller ** 3xUltras. Distance *** Motor Direction **** 3xPush buttons
***** PWM, encoder etc.
*
**
***
*****
JST-XH 2.5mm
With 2,3,4,7 pins
4xSerial
****
100n
(ceramic)

## Slide 21
PWMA
DIR1A
DIR2A
The motors, the Shield & MEGA are powered by the same, 12V battery. The motor controllers are physically already separated (20cm).
I just moved the power line for the motors on the PCB to easily connect the parts (volt & current meter, fuses & screw terminal).
If I make the orange, dashed rectangle on a separated PCB (connection remain the same.) will it help ?
Junction terminal
PWMB
DIR1B
DIR2B
Motor controllers
!

## Slide 22
Junction terminal/box
12 V LiFePO4
Battery
Buck regulator
R2
R3
For battery volt meter
Shield with MEGA
ACS712
12V
5V
12V
Distance: 5 cm (2”)
10µ & 0.1µ
100µF- 470µF
5V
A0
10µ & 0.1µ
A1
2xMotor controller (2x15A)
2x15A fuses
Top & Bottom cupper layers with max. pour, connected with array of vias
For battery amp meter
3mm trace
1mm trace
3mm trace
1mm trace
Distance: 5 cm (2”)

## Slide 23
Junction terminal/box
12 V LiFePO4
Battery
Buck regulator
R2
R3
For battery volt meter
Shield with MEGA
ACS712
12V
5V
12V
Distance: 5 cm (2”)
5V
A0
A1
2xMotor controller (2x15A)
2x15A fuses
For battery amp meter
Distance: 5 cm (2”)

## Slide 24
Shield with MEGA
Junction terminal
12 V LiFePO4
Battery
Buck regulator
R2
R3
For battery volt meter
ACS712
12V
5V
12V
Distance: 5 cm (2”)
100µF- 470µF
5 V
A0
A1
2x15A fuses
For battery ampere meter
1 A
10µ & 0.1µ ǁ
10µ & 0.1µ ǁ
2xMotor controller (2x15A)
Distance: 5 cm (2”)

## Slide 25
Junction terminal/box
12 V LiFePO4
Battery
Buck regulator
R2
R3
For battery volt meter
Shield
ACS712
12V
5V
12V
Distance: 5 cm (2”)
10µ & 0.1µ
100µF- 470µF
5Vin
GND
MCU
A0
10µ & 0.1µ
A1
2xMotor controller (2x15A)
2x15A fuses
Top & Bottom cupper layers with max. pour, connected with array of vias
For battery amp meter
3mm trace
1mm trace
3mm trace
1mm trace
Distance: 5 cm (2”)

## Slide 26
PCB - Junction terminal
12 V LiFePO4
Battery
Buck regulator
R2
R3
For battery volt meter
PCB - Shield
ACS712
12V
5V
12V
Distance: 5 cm (2”)
5Vin
GND
MCU
A0
A1
2xMotor controller (2x15A)
2x15A fuses
For battery amp meter
Distance: 5 cm (2”)
Motor GND
signal GND

## Slide 27
PCB - Junction terminal
12 V LiFePO4
Battery
Buck regulator
For battery volt meter
PCB - Shield
ACS712
12V
5V
12V
Distance: 5 cm (2”)
5Vin
GND
MCU
A0
A1
2xMotor controller (2x15A)
2x15A fuses
For battery amp meter
Distance: 5 cm (2”)
MCU GND
signal GND
100µF- 470µF
12V
R2
R3
0.1µ

## Slide 28
assuming all the parts (including the buck and the acs) should be mounted on a shield for an arduino or a raspi. I don’t know the pinning so here they end somewhere in the connector
Here you have short tracks of high current, not flowing over the whole board. You can make them nearly arbitrary wide and have them in parallel on top and bottom. R3 and the cap are as close as possible to the MCU. The MCU gets a possibly clean supply directly from the battery terminals. You might use a LM7805 instead of the buck since if you have motors of 180 watts there is no need to save one for the regulator.

## Slide 29
PCB - Junction terminal
12 V LiFePO4
Battery
Buck regulator
For battery volt meter
PCB – Shield
ACS712
12V
5V
12V
+5V GND
MCU
A0
A1
For battery amp meter
Distance: 5 cm (2”)
MCU GND
signal GND
2xMotor controller (2x15A)
2x15A fuses
12V
R2
R3
C
100µF- 470µF
LM 7805
5V
From buck converter
JST-XH 2.5mm
With 2,3,4,7 pins
B
A

## Slide 30
PCB - Junction terminal
12 V LiFePO4
Battery
Buck regulator
For battery volt meter
PCB – Shield
ACS712
12V
5V
12V
+5V GND
MCU
A1
For battery amp meter
Distance: 5 cm (2”)
MCU GND
signal GND
2xMotor controller (2x15A)
2x15A fuses
12V
R2
R3
100µF- 470µF
LM 7805
5V
From buck converter
JST-XH 2.5mm
With 2,3,4,7 pins
10µ & 0.1µ
100µF- 470µF
0.1µ
A0

## Slide 32
3mm trace on top & bottom copper + vias

## Slide 33
1N4001
R1
R2
12V
LiFePO4
78033V3
To buck converter
Current measurement
1k
For external reference
15 A
1 A
To 2 x motor controller power
15 A
From buck converter
100n
(ceramic)
For battery volt meter
3xI2C
* 3xUltras. Distance ** Motor Direction *** Push buttons
**** Encoder, PWM
*
**
***
****
B
A
JST-XH 2.5mm
With 2,3,4,6 pins
4xSerial

## Slide 34
batVoltage = 10 - 14.6V
(4 cells of LiFePO4)
Arduino MEGA
GND
A0
Vin
+5V
R1
R2
(The divider is required to measure the battery voltage.)
Sensor(s)
+5V
GND
Sig
Boundary of the Shield
switch mode "buck" regulator
1N4001
2 x DC motor controller
2 x 12V DC motors
2 x rated 4.3A
2xDIR1 2xDIR2
2xPWM
30 A (2 x 15 A)
2 A

## Slide 35
Arduino MEGA
batVoltage = 14.6 - 10 V
R2
R3
GND
A0
A0volt
Vin
20k
51k
A0 volt max (shall be 0.3 V less than V REF (4.1V) => 3.8 V
13.5V*20k/(20k+51k) = 3.802V
100n
(ceramic)
Isupply
AREF
R1
1k
LM4040 AIZ -4.1 (4.096 V +/- 0.1%)
Operating: from 60 μA to 15 mA
VR1 = 5V - 4.1V = 0.9V
+5V
I1= 0.9V / 1k = 900 µA
I3= 4.1V / 32k = 128 µA
I2= 900 µA - 128 µA = 772 µA
Select first this diode to measure near to the desired voltage:
= 4.1V
I1= 2.5V / 1k = 2500 µA
I3= 2.5V / 32k = 78 µA
I2= 2500 µA - 78 µA = 2422 µA
VR1 = 5V – 2.5V = 2.5V

## Slide 36
DS18B20
Temperature sensor
Arduino MEGA
batVoltage = 14.6 - 10.0 V
R2
R3
GND
A0
Vin
20k
51k
100n
(ceramic)
AREF
1k
+5V
R1
LM4040 AIZ -4.1 (4.096 V +/- 0.1%)
D2

## Slide 37
Here is my approach:
The battery discharge curve depending on a lot of parameters (temperature, chemistry, charge & discharge rates etc.)
The most significant from my point of view is the temperature, which can be relatively easily and accurately involved in capacity calculation as well.
So first of all everybody, who will follow the next steps, have to have the discharge curve for his own battery and correct the figures accordingly to avoid any error.
Take the curve and specific temperature, split in three or more sections. Take and values manually and fetch in tables.
Do the regression (insert trend line) with a software (Excel etc.) and make the equation for the curve visible on the graph.
Hardcode the rages and equation in the script. Measure the temperature and pass in the function.

## Slide 38
Arduino MEGA
batVoltage = 14.6 - 10 V
R2
R1
GND
A0
A0volt
Vin
20k
51k
A0 volt max=
13.5V*20k/(20k+51k) = 2.368 V
INTERNAL2V56
100n
(ceramic)
+5V
ACS712 Current sensor
DS18B20
Temperature sensor
A1
D2
Isupply
Tbattery

## Slide 39
Load current (A)
Vout (V)
on INA 21X
5V
10
Load current (A)
Vout (V)
on INA 21X
5V
10

## Slide 40
INA 213
(Gain 50V/V)
batVoltage = 14.6 - 10.0 V
I load = 0-10 A (max)
batMaxCap = 12Ah
IN+
IN-
V+
GND
Ref
Out
Load
Rshunt
To ADC
on MEGA
100n
(ceramic)
bypass
Vout = (Iload * Rshunt )*Gain + Vref
Rshunt = Vout /(Iload *Gain)=
= 5V/(10A*50) = 0.01 Ω (10m Ω)
Vout

## Slide 41
Tbattery
INA 213
(Gain 50V/V)
IN+
IN-
V+
GND
Ref
Out
100n
(ceramic)
bypass
Vout
10mΩ
MEGA
R2
R3
GND
A0
Vin
20k
51k
100n
(ceramic)
R1
1k
LM4040 AIZ-4.1
+5V
D2
DS18B20
Temperature sensor
A1
AREF
Battery terminal Voltage = 14.6 - 10.0 V
Rshunt
DC motor controller
12V DC motor
DIR1 DIR2
PWM
https://www.sciencedirect.com/science/article/pii/S0307904X13000462
https://www.hindawi.com/journals/isrn/2013/953792/
4.7kΩ
pullup
LM385Z-2.5G
LM136-2.5
LM236-2.5
LM336-2.5

## Slide 42
batVoltage = 10 - 14.6V
(4 cells of LiFePO4)
Arduino MEGA
GND
A0
Vin
+5V
R1
R2
switch mode "buck" regulator
(The divider is required to measure the battery voltage.)
Sensor(s)
+5V
GND
Sig
Boundary of the Shield

## Slide 43
batVoltage = 10 - 14.6V
(4 cells of LiFePO4)
Arduino MEGA
GND
A0
Vin
+5V
R1
R2
switch mode "buck" regulator
(The divider is required to measure the battery voltage.)
Sensor(s)
+5V
GND
Sig
Boundary of the Shield
33Ω
R3
Z1
5.V / 1W

## Slide 44
Ethernet CAT 5 then put each signal SDL and SDA in separate pairs with the wire that is not carrying the signal grounded. Example: Red = SDA, Blue = SCL, The whites from each becomes Ground, the Brown and Green become 5V with there whites also grounded. This should work. P.S. You need to only ground one end of the shield wires on SCA and SCL.

## Slide 45
LiFePO4 - Solar charger

## Slide 46
http://www.electronoobs.com/eng_arduino_tut83.php
#include <Wire.h>
#include <Adafruit_ADS1015.h>
Adafruit_ADS1115 ads;
const float multiplier = 0.1875F;
void setup(void)
{
Serial.begin(9600);
// Descomentar el que interese
// ads.setGain(GAIN_TWOTHIRDS); +/- 6.144V 1 bit = 0.1875mV (default)
// ads.setGain(GAIN_ONE); +/- 4.096V 1 bit = 0.125mV
// ads.setGain(GAIN_TWO); +/- 2.048V 1 bit = 0.0625mV
// ads.setGain(GAIN_FOUR); +/- 1.024V 1 bit = 0.03125mV
// ads.setGain(GAIN_EIGHT); +/- 0.512V 1 bit = 0.015625mV
// ads.setGain(GAIN_SIXTEEN); +/- 0.256V 1 bit = 0.0078125mV
ads.begin();
}
void loop(void)
{
int16_t adc0, adc1, adc2, adc3;
adc0 = ads.readADC_SingleEnded(0);
adc1 = ads.readADC_SingleEnded(1);
adc2 = ads.readADC_SingleEnded(2);
adc3 = ads.readADC_SingleEnded(3);
Serial.print("AIN0: "); Serial.println(adc0 * multiplier);
Serial.print("AIN1: "); Serial.println(adc1 * multiplier);
Serial.print("AIN2: "); Serial.println(adc2 * multiplier);
Serial.print("AIN3: "); Serial.println(adc3 * multiplier);
Serial.println(" ");
delay(1000);
}
ASC712

## Slide 48
batVoltage = 10 - 14.6V
(4 cells of LiFePO4)
Arduino MEGA
GND
10k
10k
ASC714
ADS1115
A0
A1
A2
SDA
SCL
SDA
SCL
A3
GND
VDD
5V
100n
(ceramic)
100n
(ceramic)
Vout [Zero] = Vcc/2
(2.5V)
5V from
buck converter

## Slide 49
batVoltage = 10 - 14.6V
(4 cells of LiFePO4)
Arduino MEGA
GND
10k
10k
ASC714
ADS1115
A0
A1
A2
SDA
SCL
SDA
SCL
A3
GND
VDD
5V
100n
(ceramic)
100n
(ceramic)
Vout [Zero] = Vcc/2
(5 - 7.3 V)
5V from
buck converter

## Slide 50
Max. 5.8 V

## Slide 51
https://www.youtube.com/watch?v=FpkUXmM7mrc
ZED-F9P Base and Rover Configuration
3dr radio telemetry
28.458505
77.287437
28.458474151945538
77.28736728429794
https://www.maps.ie/coordinates.html
7 digit accuracy: 0.0000001 0.015 m 1.5 cm

## Slide 52
MCU
HITEX ShieldBuddy TC375 or on Arduino MEGA
Motor control
With encoders
Antenna
Tallysman TW7972
Antenna
Tallysman TW7972
Base station
Can’t be xNAV650
Antenna
Tallysman TW7972
Radio
not included in xNAV650
Radio
not included in xNAV650
GNSS+IMU
Multi band
BASE
ROVER
How the navigation module can communicate to the MCU ?
A: via a RS232 GPRMC NMEA
Like this: $GPRMC,001225,A,2832.1834,N,08101.0536,W,12,25,251211,1.2,E,A*03
RTK
RTK
How communicating ?
A: Using serial input on the xNAV and an independent radio receiver.

## Slide 53
Decoding results | 
Position | 28.536390°N 81.017560°W
Timestamp | Sun, 25 Dec 2011 00:12:25 UTC
Movement | Speed 12.0 kts, heading 25°
Close to | Christmas, United States
Local time | Sat, 24 Dec 2011 19:12:25 EST
Timezone | America/New_York (UTC -0500)
https://rl.se/gprmc
Dear Customer Support,
I'm looking for moving base and robot rover setup for agricultural application in remote places.
My rover is using Arduino MEGA.
Base side MCU: still to be developed.
For Base – single rover configuration I'm searching for:
Base:
multi band GNSS receiver
+ XBee (up to 10km LoS) send the RTK correction data to the rover
+ 1 antenna
(The fix location of the base to be set after (10 min - 60 min) survey.)
Rover:
multi band GNSS receiver
+XBee (up to 10km LoS) to receive the RTK data from base
+ 1 or 2 antennas
+ IMU (for heading)
Please advise for system configuration.
I would highly appreciate, if You send a block diagram about the information flow as well :-).
In case of any questions, get it touch.
Thank You very much for Your help and support in advance.
Have a nice day ahead.
With Regards,
Andras
https://www.ardusimple.com/contact/

## Slide 56
1 Time Stamp
2 validity - A-ok, V-invalid
3 current Latitude
4 North/South
5 current Longitude
6 East/West
7 Speed in knots
8 True course – Is this the true heading id degree with 0.1° accuracy ??
9 Date Stamp
10 Variation
11 East/West
12 checksum
As per last r-mail:
That’s no problem if you don’t need the full NCOM data, you can also have NMEA data output over serial or ethernet. For example you can output GPRMC NMEA messages which contain

## Slide 57
ZED-F9K & ZED-F9R has an IMU, but F9P no, because it can be base as well !
Select for
rover
Select for base
simpleRTK2B is u-blox ZED-F9P

## Slide 58
Arduino MEGA
Motor control
With encoders
Calibrated Survey GNSS Multiband antenna
simpleRTK2Blite
(ZED-F9P )
Calibrated Survey GNSS Multiband antenna
Radio
XBee LR
Radio
XBee LR
RTK+INS simpleRTK2B-F9R V3 shield in stand alone mode
BASE
ROVER
RTK
RTK
https://www.ardusimple.com/product/simplertk2b-heading-basic-starter-kit-ip67/
https://www.ardusimple.com/product/simplertk2b-f9r-v3/
https://www.ardusimple.com/product/simplertk2blite/
TXRX2
TX1RX0-3 (MEGA)
RXTX2
TXRX2
Rover pos.
Rover pos.
TX2RX
Laptop
RXTX1
(rover pos.)
(rover pos.)
(rover pos.)
(RTCM corr. data)
(RTCM corr. data)
(RTCM corr. data)
(RTCM corr. data)

## Slide 59
simpleRTK2Blite 199,00€
RTK+INS simpleRTK2B-F9R V3 486,00€
headers 5,00€
Pixhawk cable set 15,00€
XBee (LR) + Antenna 116,00€
XBee (LR) + Antenna 116,00€
Calibrated Survey GNSS Multiband antenna (IP67) 149,00€
Calibrated Survey GNSS Multiband antenna (IP67) 149,00€
Stand for survey GNSS Multiband antenna 18,00€
Stand for survey GNSS Multiband antenna 18,00€

## Slide 61
U-blox 6
Receiver description
Including protocol description
const unsigned char UBX_HEADER[] = { 0xB5, 0x62 };
struct NAV_POSLLH {
unsigned char cls;
unsigned char id;
unsigned short len;
unsigned long iTOW;
long lon;
long lat;
long height;
long hMSL;
unsigned long hAcc;
unsigned long vAcc;
};

## Slide 62
const unsigned char UBX_HEADER[] = { 0xB5, 0x62 };
struct NAV_PVT {
unsigned char cls;
unsigned char id;
unsigned short len;
unsigned long iTOW; // GPS time of week of the navigation epoch (ms)
unsigned short year; // Year (UTC)
unsigned char month; // Month, range 1..12 (UTC)
unsigned char day; // Day of month, range 1..31 (UTC)
unsigned char hour; // Hour of day, range 0..23 (UTC)
unsigned char minute; // Minute of hour, range 0..59 (UTC)
unsigned char second; // Seconds of minute, range 0..60 (UTC)
char valid; // Validity Flags (see graphic below)
unsigned long tAcc; // Time accuracy estimate (UTC) (ns)
long nano; // Fraction of second, range -1e9 .. 1e9 (UTC) (ns)
unsigned char fixType; // GNSSfix Type, range 0..5
char flags; // Fix Status Flags
unsigned char reserved1; // reserved
unsigned char numSV; // Number of satellites
used in Nav Solution
long lon; // Longitude (deg)
long lat; // Latitude (deg)
long height; // Height above Ellipsoid (mm)
long hMSL; // Height above mean sea level (mm)
unsigned long hAcc; // Horizontal Accuracy Estimate (mm)
unsigned long vAcc; // Vertical Accuracy Estimate (mm)
long velN; // NED north velocity (mm/s)
long velE; // NED east velocity (mm/s)
long velD; // NED down velocity (mm/s)
long gSpeed; // Ground Speed (2-D) (mm/s) long heading; // Heading of motion 2-D (deg) unsigned long sAcc; // Speed Accuracy Estimate unsigned long headingAcc; // Heading Accuracy Estimate unsigned short pDOP; // Position dilution of precision short reserved2; // Reserved unsigned long reserved3; // Reserved};
void loop() { if ( processGPS() ) { Serial.print("#SV: "); Serial.print(pvt.numSV); Serial.print(" fixType: "); Serial.print(pvt.fixType); Serial.print(" Date:"); Serial.print(pvt.year); Serial.print("/"); Serial.print(pvt.month); Serial.print("/"); Serial.print(pvt.day); Serial.print(" "); Serial.print(pvt.hour); Serial.print(":"); Serial.print(pvt.minute); Serial.print(":"); Serial.print(pvt.second); Serial.print(" lat/lon: "); Serial.print(pvt.lat/10000000.0f); Serial.print(","); Serial.print(pvt.lon/10000000.0f); Serial.print(" gSpeed: "); Serial.print(pvt.gSpeed/1000.0f); Serial.print(" heading: "); Serial.print(pvt.heading/100000.0f); Serial.print(" hAcc: "); Serial.print(pvt.hAcc/1000.0f); Serial.println(); }}