## Slide 1
MCU
HITEX ShieldBuddy TC375 or on Arduino MEGA
Motor control
With encoders
Antenna
Tallysman TW7972
Antenna
Tallysman TW7972
Base station
Can’t be xNAV650
Antenna
Tallysman TW7972
Radio
not included in xNAV650
Radio
not included in xNAV650
GNSS+IMU
Multi band
BASE
ROVER
How the navigation module can communicate to the MCU ?
A: via a RS232 GPRMC NMEA
Like this: $GPRMC,001225,A,2832.1834,N,08101.0536,W,12,25,251211,1.2,E,A*03
RTK
RTK
How communicating ?
A: Using serial input on the xNAV and an independent radio receiver.

## Slide 2
Decoding results | 
Position | 28.536390°N 81.017560°W
Timestamp | Sun, 25 Dec 2011 00:12:25 UTC
Movement | Speed 12.0 kts, heading 25°
Close to | Christmas, United States
Local time | Sat, 24 Dec 2011 19:12:25 EST
Timezone | America/New_York (UTC -0500)
https://rl.se/gprmc
Dear Customer Support,
I'm looking for moving base and robot rover setup for agricultural application in remote places.
My rover is using Arduino MEGA.
Base side MCU: still to be developed.
For Base – single rover configuration I'm searching for:
Base:
multi band GNSS receiver
+ XBee (up to 10km LoS) send the RTK correction data to the rover
+ 1 antenna
(The fix location of the base to be set after (10 min - 60 min) survey.)
Rover:
multi band GNSS receiver
+XBee (up to 10km LoS) to receive the RTK data from base
+ 1 or 2 antennas
+ IMU (for heading)
Please advise for system configuration.
I would highly appreciate, if You send a block diagram about the information flow as well :-).
In case of any questions, get it touch.
Thank You very much for Your help and support in advance.
Have a nice day ahead.
With Regards,
Andras
https://www.ardusimple.com/contact/

## Slide 5
1 Time Stamp
2 validity - A-ok, V-invalid
3 current Latitude
4 North/South
5 current Longitude
6 East/West
7 Speed in knots
8 True course – Is this the true heading id degree with 0.1° accuracy ??
9 Date Stamp
10 Variation
11 East/West
12 checksum
As per last r-mail:
That’s no problem if you don’t need the full NCOM data, you can also have NMEA data output over serial or ethernet. For example you can output GPRMC NMEA messages which contain

## Slide 6
ZED-F9K & ZED-F9R has an IMU, but F9P no, because it can be base as well !
Select for
rover
Select for base
simpleRTK2B is u-blox ZED-F9P

## Slide 7
Arduino MEGA
Motor control
With encoders
Calibrated Survey GNSS Multiband antenna
simpleRTK2Blite
(ZED-F9P )
Calibrated Survey GNSS Multiband antenna
Radio
XBee LR
Radio
XBee LR
RTK+INS simpleRTK2B-F9R V3 shield in stand alone mode
BASE
ROVER
RTK
RTK
https://www.ardusimple.com/product/simplertk2b-heading-basic-starter-kit-ip67/
https://www.ardusimple.com/product/simplertk2b-f9r-v3/
https://www.ardusimple.com/product/simplertk2blite/
TXRX2
TX1RX0-3 (MEGA)
RXTX2
TXRX2
Rover pos.
Rover pos.
TX2RX
Laptop
RXTX1
(rover pos.)
(rover pos.)
(rover pos.)
(RTCM corr. data)
(RTCM corr. data)
(RTCM corr. data)
(RTCM corr. data)
https://www.sparkfun.com/products/16481
https://www.sparkfun.com/products/16344

## Slide 9
simpleRTK2Blite 199,00€
RTK+INS simpleRTK2B-F9R V3 486,00€
headers 5,00€
Pixhawk cable set 15,00€
XBee (LR) + Antenna 116,00€
XBee (LR) + Antenna 116,00€
Calibrated Survey GNSS Multiband antenna (IP67) 149,00€
Calibrated Survey GNSS Multiband antenna (IP67) 149,00€
Stand for survey GNSS Multiband antenna 18,00€
Stand for survey GNSS Multiband antenna 18,00€
ZED-F9P-02B Rs15 000
ZED-F9R-02B Rs15 000
Mouser.com
https://www.gnss.store/gnss-gps-modules/134-ublox-zed-f9r-elt0117.html
249,99 € tax excl
ZED-F9R
ZED-F9P
https://www.gnss.store/gnss-gps-modules/99-ublox-zed-f9p-rtk-gnss-receiver-board-with-sma-base-or-rover.html
209,99 € tax excl.
189,99 € tax excl.
https://www.gnss.store/rf-gps-antennas/140-elt0123.html
https://www.sparkfun.com/products/16344
GPS Development Tools SparkFun GPS-RTK-SMA Breakout - ZED-F9P
16,796 = 190 EUR
SparkFun Accessories SparkFun GPS-RTK Dead Reckoning Breakout - ZED-F9R (Qwiic) 21,644 = 242 EUR

## Slide 10
https://www.tanotis.com/products/sparkfun-gps-rtk-sma-breakout-zed-f9p-qwiic
Rs 30 000
Rs 24 000
https://www.tanotis.com/products/sparkfun-xbee-3-module-rp-sma-antenna
2,670
https://www.tanotis.com/products/sparkfun-gps-rtk-dead-reckoning-breakout-zed-f9r-qwiic
https://www.tanotis.com/products/genuine-sparkfun-sparkfun-xbee-explorer-regulated
1,115
https://www.tanotis.com/products/genuine-sparkfun-interface-cable-sma-to-u-fl

## Slide 12
https://www.tanotis.com/products/sparkfun-gps-rtk-dead-reckoning-breakout-zed-f9r-qwiic?gclid=Cj0KCQjwsqmEBhDiARIsANV8H3aChXVXNU2BihZM26-xD0q3iITXEzSM_eGfl2cql53cwCX6hNuwVzwaAlHJEALw_wcB
GPS & IMU to rover
RTK in
from radio
Rover msg to radio
RTK in
from radio
Rover msg to radio
GPS & IMU to rover

## Slide 13
U-blox 6
Receiver description
Including protocol description
const unsigned char UBX_HEADER[] = { 0xB5, 0x62 };
struct NAV_POSLLH {
unsigned char cls;
unsigned char id;
unsigned short len;
unsigned long iTOW;
long lon;
long lat;
long height;
long hMSL;
unsigned long hAcc;
unsigned long vAcc;
};

## Slide 14
const unsigned char UBX_HEADER[] = { 0xB5, 0x62 };
struct NAV_PVT {
unsigned char cls;
unsigned char id;
unsigned short len;
unsigned long iTOW; // GPS time of week of the navigation epoch (ms)
unsigned short year; // Year (UTC)
unsigned char month; // Month, range 1..12 (UTC)
unsigned char day; // Day of month, range 1..31 (UTC)
unsigned char hour; // Hour of day, range 0..23 (UTC)
unsigned char minute; // Minute of hour, range 0..59 (UTC)
unsigned char second; // Seconds of minute, range 0..60 (UTC)
char valid; // Validity Flags (see graphic below)
unsigned long tAcc; // Time accuracy estimate (UTC) (ns)
long nano; // Fraction of second, range -1e9 .. 1e9 (UTC) (ns)
unsigned char fixType; // GNSSfix Type, range 0..5
char flags; // Fix Status Flags
unsigned char reserved1; // reserved
unsigned char numSV; // Number of satellites
used in Nav Solution
long lon; // Longitude (deg)
long lat; // Latitude (deg)
long height; // Height above Ellipsoid (mm)
long hMSL; // Height above mean sea level (mm)
unsigned long hAcc; // Horizontal Accuracy Estimate (mm)
unsigned long vAcc; // Vertical Accuracy Estimate (mm)
long velN; // NED north velocity (mm/s)
long velE; // NED east velocity (mm/s)
long velD; // NED down velocity (mm/s)
long gSpeed; // Ground Speed (2-D) (mm/s) long heading; // Heading of motion 2-D (deg) unsigned long sAcc; // Speed Accuracy Estimate unsigned long headingAcc; // Heading Accuracy Estimate unsigned short pDOP; // Position dilution of precision short reserved2; // Reserved unsigned long reserved3; // Reserved};
void loop() { if ( processGPS() ) { Serial.print("#SV: "); Serial.print(pvt.numSV); Serial.print(" fixType: "); Serial.print(pvt.fixType); Serial.print(" Date:"); Serial.print(pvt.year); Serial.print("/"); Serial.print(pvt.month); Serial.print("/"); Serial.print(pvt.day); Serial.print(" "); Serial.print(pvt.hour); Serial.print(":"); Serial.print(pvt.minute); Serial.print(":"); Serial.print(pvt.second); Serial.print(" lat/lon: "); Serial.print(pvt.lat/10000000.0f); Serial.print(","); Serial.print(pvt.lon/10000000.0f); Serial.print(" gSpeed: "); Serial.print(pvt.gSpeed/1000.0f); Serial.print(" heading: "); Serial.print(pvt.heading/100000.0f); Serial.print(" hAcc: "); Serial.print(pvt.hAcc/1000.0f); Serial.println(); }}

## Slide 18
AECC0502GB – C
https://www.mouser.in/ProductDetail/ABRACON/AECC0502GBS-S?qs=eP2BKZSCXI6WHWNXCHgIFA%3D%3D
Ultra- Low Profile
Active GNSS
GPS : L1/L2
GLONASS : G1/G2
BEIDOU/Compass : B1/B2/B3
GALIELO : E1/E5b
AEACMK0660746-SG4
https://www.mouser.in/ProductDetail/ABRACON/AEACMK0660746-SG4?qs=Cb2nCFKsA8qSI2ROBfTxbg%3D%3D
GPS: L1/L2/L5/L6
BEIDOU: B1/B2/B3
GLONASS: L1/L2
Galileo: L1/E5b/E5a
QZSS: L1/L2/L5/L6
AEAGMK148060-S1575
https://www.mouser.in/ProductDetail/ABRACON/AEAGMK148060-S1575?qs=fAHHVMwC%252Bbg%2FdxTyG9xYxQ%3D%3D

## Slide 19
https://www.mouser.in/ProductDetail/ArduSimple/AS-ANT2B-SUR-L1L2-25SMA-00?qs=vHuUswq2%252BswBsit1qMDm7Q%3D%3D
GPS L1/L2
GLONASS L1/L2
COMPASS B1/B2/B3
Galileo E1/E5b/E6
TNC Female (2.5m cable to SMA male included)
SMA (F, jack) Bulkhead Straight
. RG58 Cable
Heatshrink
Heatshrink
.SMA (M, plug) Bulkhead Straight